32-bit Architecture Specification

- RISC architecture, load/store oriented
- 32-bit data, address and instruction width
- Supports up to 4Gb RAM
- 16 internal GP registers
- Supports addition, subtraction, AND, OR, XOR, NOT, shift left/right

Instruction Set:

Note: → Reg = Register
        Imme. = Immediate value
        DC = Don't care

Syntax:	Description:
LD Reg1, Reg2	Loads data from memory address stored in Reg2 into Reg1
ST Reg1, Reg2	Stores data from Reg1 into memory address stored in Reg2
ADD Reg1, Reg2, Reg3	Adds Reg1 and Reg2, stores value in Reg3
SUB Reg1, Reg2, Reg3	Subs Reg2 from Reg1, stores value in Reg3
AND Reg1, Reg2, Reg3	ANDs Reg1 and Reg2, stores value in Reg3
OR Reg1, Reg2, Reg3	ORs Reg1 and Reg2, stores value in Reg3
XOR Reg1, Reg2, Reg3	XORs Reg1 and Reg2, stores value in Reg3
SFR Reg	Shifts Reg right 1 bit
SFL Reg	Shifts Reg left 1 bit
MOV Reg1, Reg2	Moves Reg2 into Reg1
MVL Reg, Imme.	Moves Imme. Into lower 16 bits of Reg, does not overwrite existing higher 16 bits
MVH Reg, Imme.	Moves Imme. Into higher 16 bits of Reg, does not overwrite the lower 16 bits
CLR Reg	Clears Reg
JMP Reg	Absolute jump to memory address stored in Reg
JEZ Reg1, Reg2	Jumps to memory address stored in Reg2 if the value in Reg1 is equal to zero
JGZ Reg1, Reg2	Jumps to memory address stored in Reg2 if the value in Reg1 is greater than zero
JLZ Reg1, Reg2	Jumps to memory address stored in Reg2 if the value in Reg1 is less than zero
HLT	Halts the system
NOP	No operation

Addressing and Data:

Registers: → 8-bit, #0 → #15 general purpose, #255 program counter
Addresses:→ 32-bit, #0 → #65535
Immediate values: → Move command → 16-bit, signed -32768 → 32767, unsigned 0 → 65535

Instruction Layout:

8	8	8	8
ID	R1	R2	R3	→ ADD, SUB, AND, OR, XOR
ID	R1	R2	DC	→ LD, ST, JEZ, JGZ, JLZ, MOV
ID	R1	Immediate		→ MVL, MVH
ID	R1	DC		→ SFR, SFL, CLR, JMP
ID	DC			→ HLT, NOP

ID Layout:

- There will be four types of instructions: - 00→Jumps and misc.
        - 01→Arithmetic
        - 10→Logic
        - 11→ Memory management

2	6
Type	Binary assignment

Instruction:	ID:
NOP	00-000000
JMP	00-000001
JEZ	00-000010
JGZ	00-000011
JLZ	00-000100
HLT	00-000101

ADD	01-000000
SUB	01-000001

AND	10-000000
OR	10-000001
XOR	10-000010
SFL	10-000011
SFR	10-000100

LD	11-000000
ST	11-000001
MOV	11-000010
MVL	11-000011
MVH	11-000100
CLR	11-000101

External Connections/ IO:

Name (Abbrev.) - (Size in bits):	Direction:	Description:
Clock – (clk) - (1)	Input	The system can take in a clock signal that it can distribute, divide, stop etc.
Reset – (rst) - (1)	Input	This is the master reset of the system, it wipes all internal registers to zero, clears the bus, ALU and program counter, turns off all control signals.
Data in bus – (dib) - (32)	Input	This is the 32-bit bus that carries data into the system.
Data out bus – (dob) - (32)	Output	This is the 32-bit bus that carries data from the system.
Address bus – (ab) - (32)	Output	This is the 32-bit bus that carries the addresses the system will use to the respective external devices.
Control bus – (cb) - (tbd)	Input/Output	This is the n-bit bus that carries all the control signals to the external devices, eg. R/W request, R/W ack etc.
Halt – (hlt) – (1)	Output	This is the halt signal that feeds to the external oscillator to halt the system.

Improvements:

- Additional Arithmetic/Logic → Floating point, comparators, multiply, divide
- Give arithmetic/logic instructions immediate value capabilities
- Interrupt capabilities
- I2C/SPI/UART/USART
- PWM
- 2 → 4 Parallel I/O Ports
- Increased number of internal registers
- Special Function Registers → PSW, Interrupts, Null
- Timers
- Sleep modes
- Pipe-lining → Speculative
- Threading and scalability